- Manipulando bits

Obervação quanto aos pinos:

Pino	Nome	3,3V	5,0V		Pino	Nome	3,3V	5,0V
10	PA0	x			20	PB2	x	x
11	PA1	x			39	PB3	x	x
12	PA2	x			40	PB4	x	x
13	PA3	x			41	PB5	x
14	PA4	x			42	PB6	x	x
15	PA5	x			43	PB7	x	x
16	PA6	x			45	PB8	x	x
17	PA7	x			46	PB9	x	x
29	PA8	x	x		21	PB10	x	x
30	PA9	x	x		22	PB11	x	x
31	PA10	x	x		25	PB12	x	x
32	PA11	x	x		25	PB13	x	x
33	PA12	x	x		27	PB14	x	x
34	PA13	x	x		28	PB15	x	x
37	PA14	x	x		2	PC13	x
38	PA15	x	x		3	PC14	x
18	PB0	x			4	PC15	x
19	PB1	x

Na biblioteca main.h

#define EN1_Pin GPIO_PIN_0
#define EN1_GPIO_Port GPIOD
#define EN2_Pin GPIO_PIN_1
#define EN2_GPIO_Port GPIOD
#define EN4_Pin GPIO_PIN_14
#define EN4_GPIO_Port GPIOC

-- Setar um bit do port:

HAL_GPIO_WritePin(EN4_GPIO_Port, EN4_Pin, GPIO_PIN_SET);

-- Setar alguns bits do port:

HAL_GPIO_WritePin(GPIOD, EN1_Pin|EN2_Pin, GPIO_PIN_RESET);

-- Resetar um bit do port:

HAL_GPIO_WritePin(EN4_GPIO_Port, EN4_Pin, GPIO_PIN_RESET);

-- Resetar alguns bits do port:

HAL_GPIO_WritePin(GPIOA, D0_Pin|D1_Pin|D2_Pin|D3_Pin
        |D4_Pin|D5_Pin|D6_Pin|D7_Pin, GPIO_PIN_RESET);

- Lendo um bit do port:

uint8_t var;
var = HAL_GPIO_ReadPin(PP1_GPIO_Port, PP1_Pin);

-- Escrevendo de uma só vez no port:

GPIOA-> ODR = 0x0000; //Escreve 0000h em GPIOA
GPIOA-> ODR = 0b0000000000010000;

- Tipo de variáveis

Type	Size in bits	Natural alignment in bytes	Range of values
char	8	1 (byte-aligned)	0 to 255 (unsigned) by default. / –128 to 127 (signed) when compiled with --signed_chars.
signed char	8	1 (byte-aligned)	–128 to 127
unsigned char	8	1 (byte-aligned)	0 to 255
(signed) short	16	2 (halfword-aligned)	–32,768 to 32,767
unsigned short	16	2 (halfword-aligned)	0 to 65,535
(signed) int	32	4 (word-aligned)	–2,147,483,648 to 2,147,483,647
unsigned int	32	4 (word-aligned)	0 to 4,294,967,295
(signed) long	32	4 (word-aligned)	–2,147,483,648 to 2,147,483,647
unsigned long	32	4 (word-aligned)	0 to 4,294,967,295
(signed) long long	64	8 (doubleword-aligned)	–9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
unsigned long long	64	8 (doubleword-aligned)	0 to 18,446,744,073,709,551,615
float	32	4 (word-aligned)	1.175494351e-38 to 3.40282347e+38 (normalized values)
double	64	8 (doubleword-aligned)	2.22507385850720138e-308 to 1.79769313486231571e+308 (normalized values)
long double	64	8 (doubleword-aligned)	2.22507385850720138e-308 to 1.79769313486231571e+308 (normalized values)
wchar_t	16 / 32	2 (halfword-aligned) / 4 (word-aligned)	0 to 65,535 by default. / 0 to 4,294,967,295 when compiled with --wchar32.
All pointers	32	4 (word-aligned)	Not applicable.
bool (C++ only)	8	1 (byte-aligned)	false or true
_Bool (C onlya)	8	1 (byte-aligned)	false or true

## Instruções:

if se verdadeiro
 if(HAL_GPIO_ReadPin(CHA_GPIO_Port, CHA_Pin))
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }

if se falso
 if(!HAL_GPIO_ReadPin(CHA_GPIO_Port, CHA_Pin))
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }

- Trabalhando com memória:

//Leitura da posição 0x08010000
uint8_t data;
data = *(uint8_t *)0x08010000;

- Manipulando registros

uint32_t pageAddress

pageAddress = 0x08010000;

FLASH->AR = pageAddress; //pageAddress recebe o endereço 08010000

FLASH->CR |= FLASH_CR_PER; //set bit PER of register FLASH_CR
FLASH->CR &= ~FLASH_CR_PER;//reset bit PER of register FLASH_CR

//Se o bit EOP do registro FLASH_SR for 1
if(FLASH->SR & FLASH_SR_EOP)
{
FLASH->SR &= ~FLASH_SR_EOP;
FLASH->CR &= ~FLASH_CR_PER;
return 1;
}

- Manipulando variáveis

number é a variável
x posição do bit

-- Setando um bit:

number |= 1 << x;

-- Resetando um bit:

number &= ~(1 << x);

- Alterando um bit:

number ^= 1 << x;

-- Testando um bit:

bit = (number >> x) & 1;

- Alterando o enésimo bit para x:

número ^ = (-x ^ número) & ( 1 << n);

-- Lendo de uma só vez no port:

uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

Exemplo:

main:

/* USER CODE BEGIN PV */
uint16_t var;
/* USER CODE END PV */

...

/* USER CODE BEGIN PFP */
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx);
/* USER CODE END PFP */

…

  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 var = GPIO_ReadInputData(GPIOB);
  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
//- Função para ler um port de 16 bits:
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

/* USER CODE END 4 */

- Função para ler um port de 16 bits:

uint16_t read_word(void)
{
   volatile uint16_t data = 0;
   data = (uint16_t)GPIOD->IDR & 0xffff;
   return data;
}

-- Função para escrever em um port de 16 bits:

void write_word(uint16_t cmd)
{
   //GPIOA->ODR = cmd & 0xffff;
   GPIOA->ODR = cmd;
}

- Função para ler dois port’s em 8 bits e guardar em uma variável de 16 bits:

uint16_t read_world_2(void)
{
    volatile uint16_t data = 0;
    data = (uint16_t)GPIOD->IDR & 0x00ff; //lsb
    data |= (uint16_t)GPIOA->IDR << 8 ; // msb
    return data;
}

- Função para escrever em dois port’s em 8 bits de uma variável de 16 bits:

void write_world_2(uint16_t cmd)
{
    GPIOD->ODR = cmd & 0x00ff; //lsb
    GPIOA->ODR = (GPIOA->ODR & 0x00ff) | (cmd >> 8); //msb
}

- Exemplo de utilização de definições

# Significado do sufixo U
Significa unsigned.
Quando você declara uma constante, também pode especificar seu tipo. Outro exemplo comum é o L que significa long. (e você deve colocá-lo duas vezes para especificar uma constante de 64 bits).

Exemplo: 1ULL

Constantes inteiras em C e C ++ podem opcionalmente ter vários sufixos:
123u o valor 123 é um int
123l não assinado (que é um L minúsculo) 123 é um
123L longo assinado idem
123uL não assinado longo
123LL um longo assinado, um valor de 64 bits ou 128 bits (dependendo do ambiente)
123uLL não assinado há muito tempo

# Qual é a diferença entre typedef e enum?

enum define um nome de tipo automaticamente, enquanto no caso de typedef que define um novo tipo de dados que pode ser de qualquer tipo de tipo de dados de modo que nós não têm declará-la explicitamente everytime.

Exemplo utilizando o registro FLASH_CR (Flash control register) (PM0075)

Address offset: 0x10
Reset value: 0x0000 0080

Flash control register (FLASH_CR)
Address offset: 0x10
Reset value: 0x0000 0080

31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16
Reserved
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
Reserved			EOPIE	Res.	ERRIE	OPTWR E	Res.	LOCK	STRT	OPTER	OPT / PG	Res.	MER	PER	PG
			rw		rw	rw		rw	rw	rw	rw		rw	rw	rw

Bits 31:13 Reserved, must be kept cleared.

Bit 12 EOPIE: End of operation interrupt enable
This bit enables the interrupt generation when the EOP bit in the	FLASH_SR register goes to 1.
0: Interrupt generation disabled
1: Interrupt generation enabled

Bit 11 Reserved, must be kept cleared

Bit 10 ERRIE: Error interrupt enable
This bit enables the interrupt generation on an FPEC error (when	PGERR / WRPRTERR are set in the FLASH_SR register).
0: Interrupt generation disabled
1: Interrupt generation enabled

Bit 9 OPTWRE: Option bytes write enable
When set, the option bytes can be programmed. This bit is set on	writing the correct key sequence to the FLASH_OPTKEYR register.
This bit can be reset by software

Bit 8 Reserved, must be kept cleared.

Bit 7 LOCK: Lock
Write to 1 only. When it is set, it indicates that the FPEC and	FLASH_CR are locked. This bit is reset by hardware after detecting	the unlock sequence. In the event of unsuccessful unlock operation,	this bit remains set until the next reset.

Bit 6 STRT: Start
This bit triggers an ERASE operation when set. This bit is set only	by software and reset when the BSY bit is reset.

Bit 5 OPTER: Option byte erase
Option byte erase chosen.

Bit 4 OPTPG: Option byte programming
Option byte programming chosen.

Bit 3 Reserved, must be kept cleared.

Bit 2 MER: Mass erase
Erase of all user pages chosen.

Bit 1 PER: Page erase
Page Erase chosen.

Bit 0 PG: Programming
Flash programming chosen.

Arquivo: definições.h

typedef struct
{
  __IO uint32_t ACR;
  __IO uint32_t KEYR;
  __IO uint32_t OPTKEYR;
  __IO uint32_t SR;
  __IO uint32_t CR;
  __IO uint32_t AR;
  __IO uint32_t RESERVED;
  __IO uint32_t OBR;
  __IO uint32_t WRPR;
} FLASH_TypeDef;

#define PERIPH_BASE 0x40000000UL
#define AHBPERIPH_BASE (PERIPH_BASE + 0x00020000UL)
#define FLASH_R_BASE (AHBPERIPH_BASE + 0x00002000UL)

#define FLASH ((FLASH_TypeDef *)FLASH_R_BASE)

#define FLASH_CR_PG_Pos (0U)
#define FLASH_CR_PG_Msk (0x1UL << FLASH_CR_PG_Pos) /*!< 0x00000001 */
#define FLASH_CR_PG FLASH_CR_PG_Msk /*!< Programming */

#define FLASH_CR_LOCK_Pos (7U)
#define FLASH_CR_LOCK_Msk (0x1UL << FLASH_CR_LOCK_Pos) /*!< 0x00000080 */
#define FLASH_CR_LOCK FLASH_CR_LOCK_Msk /*!< Lock */

Exemplo de utilização:

FLASH->CR &= ~FLASH_CR_PG; // ensure PG is low
FLASH->CR |= FLASH_CR_LOCK; // set the LOCK bit

while(FLASH->SR & FLASH_SR_BSY)
{
if(--timeout == 0)
{
return -1;
}
}

-----------------------------------------

Definições da estrutura do GPIO (ex GPIOC)

typedef struct
{
  __IO uint32_t CRL;
  __IO uint32_t CRH;
  __IO uint32_t IDR;
  __IO uint32_t ODR;
  __IO uint32_t BSRR;
  __IO uint32_t BRR;
  __IO uint32_t LCKR;
} GPIO_TypeDef;

#define PERIPH_BASE 0x40000000UL /*!< Peripheral base address in the alias region */

#define APB2PERIPH_BASE (PERIPH_BASE + 0x00010000UL)

#define GPIOC_BASE (APB2PERIPH_BASE + 0x00001000UL)

#define GPIOC ((GPIO_TypeDef *)GPIOC_BASE)

Exemplo de uso:

GPIOC-> ODR = 0x0000; //Escreve 0000h em GPIOC

volatile uint16_t data = 0;
data = (uint16_t)GPIOD->IDR & 0x00ff; //lsb
data |= (uint16_t)GPIOA->IDR << 8 ; // msb

0x4000 0000
0x0001 0000
0x0000 1000
-----------
0x4001 1000

Exemplos de programas

- Exemplo 1

Escrevendo diretamente na porta A

main.c

/* USER CODE BEGIN PV */
uint16_t cmd;
/* USER CODE END PV */

...

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 cmd=0x5555;
 write_word(cmd);
 HAL_Delay(1000);
 cmd=0xAAAA;
 write_word(cmd);
 HAL_Delay(1000);
  }
  /* USER CODE END 3 */

...

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 2

Deslocamento de bits para a esquerda

main.c

/* USER CODE BEGIN PV */
uint8_t x=0;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x);
 write_word(cmd);
 HAL_Delay(100);

 x++;

 if(x == 10)
 {
 x=0;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 3

Deslocamento de bits para a direita

main.c

/* USER CODE BEGIN PV */
int x=9;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x);
 write_word(cmd);
 HAL_Delay(100);

 x--;

 if(x < 10)
 {
 x=9;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 4

Deslocamento de bits para a direita e para a esquerda

main.c

/* USER CODE BEGIN PV */
uint8_t x1=5, x2=4, y=0;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x1;
 cmd |= 1 << x2;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x1);
 cmd &= ~(1 << x2);
 write_word(cmd);
 HAL_Delay(100);

 x1++;
 x2--;
 y++;

 if(y == 5)
 {
 y=0;
 x1=5;
 x2=4;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 5

Lendo um port inteiro de 16 bits, armazenando em uma variável e testando o 10 bit. Caso seja 1, liga o bit L0. Caso seja 0, desliga o bit L0

main.h

#define L0_Pin GPIO_PIN_0
#define L0_GPIO_Port GPIOA

main.c

/* USER CODE BEGIN PV */
uint8_t x;
uint16_t var;
/* USER CODE END PV */

…

/* USER CODE BEGIN PFP */
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx);
/* USER CODE END PFP */

…

  /* Infinite loop */
  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 var = GPIO_ReadInputData(GPIOB);

 x = 10;
 if((var >> x) & 1)
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }
  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
//- Função para ler um port de 16 bits:
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

/* USER CODE END 4 */